PMAS Velocity Intake System Installation Instructions

Thank you for purchasing the PMAS Velocity Intake System for the 2015 Mustang 5.0. Please read these installation instructions carefully before proceeding.

Software instructions

1. Please follow link to download programmable software files.

http://www.pmas-maf.com/product/velocity-air-intake-systems

Please click and download each of the following file links

Programmable Mass Air Software

Airflow Sensor Files

Temp and Output Files

2. Extract 3 folders by right-clicking and selecting Extract

3. Open HPX-V1.3 folder and run setup. Programmable Mass Air program should auto run upon completion of setup.

4. Verify Maf serial number on flow sheet supplied with your Programmable Mass Airflow sensor. Look in airflow sensor files for corresponding number. Place this file in a new folder on your desktop named PMAS

5. Move all temp and Output files into PMAS folder.

6. In Program click load CSV under maf in table select correct Maf file with correct serial number.

7. Click load CSV under maf out table and select 2015 Mustang Stock

8. Click load CSV under Temp in table and select temp in three

9. Click load CSV under RES out table and select temp out 2015 Mustang.

10. Under V GM KV make sure GM is selected

11. Under input filter select light

12. Under Windows start menu click on devices and printers

13. Connect USB cable to computer and other end of USB Cable to Programmable Maf box supplied with kit, Windows should install device drivers. This step may take awhile. 14. Click on Windows start menu, then devices and printers. A new icon names ‘USB serial port’ should be showing with a COM Port number listed below. Note this port number.

15. In PMAS software select correct COM Port number.

16. Click Connect, status should change to connected.

17. Click Re Config.

18. Click Write Config.

19. You have now updated your Programmable Mass Air, please continue with the remainder of the installation.

Step1: Remove decorative engine cover by lifting it and sliding it under the strut tower

Brace.

2: Disconect Mass airflow sensor connector

3: Remove hose clamp at air box next to mass airflow sensor

4: Remove intake hose from air box

5: Release air box snaps holding down factory air box lid, and remove air box lid.

6: Remove single bolt holding lower air box to inner fender and remove lower air box.

7: Remove intake tube clamp at throttle body

8: Remove intake tube from Throttle body

9: Carefully remove plastic clips attaching three hoses to intake tube.

10: Remove hoses from intake tube

11: Remove sound tube from intake tube.

12: Remove intake tube. If desired remove entire intake tube from attachment at firewall.

13: Remove two bolts from coolant reservoir, install supplied reservoir relocation bracket using supplied bolts.

14 Install coolant reservoirs onto relocation bracket using factory bolts.

15: Install PMAS heat shield and install one hold down bolt in original location.

16: Slide large 5” hose coupling onto PMAS intake tube.

17: Slide PMAS Velocity Mass Air flow Sensor into 5” coupling, do not tighten any clamps at this time.

18: Carefully slide throttle body end of PMAS intake tube onto Throttle body, and lower entire assembly into the lower air box. Make sure that the portion of the maf sensor with the electrical connection in pointing up towards the hood.

19: This step in very important. Make sure that throttle body coupling is pressed firmly and completely onto throttle body. If done correctly the large intake elbow will be touching the top of the fan shroud (see picture) this will ensure proper hood clearance. Tighten throttle body clamp.

20: Make sure maf is correctly oriented and placed, then tighten down two 5” hose clamps.

21: Reinstall three hoses onto intake tube and sound tube if desired. Reinstall hose clips.

22: Connect female end of maf controller to PMAS Velocity Maf, connect male end of maf controller to factory maf connector.

23: By hand, lower hood until hoods stops. Gently press hood down by hand until hood body lines match up. This will assure hood clearance. If hood does not clear, then repeat step 16. We are not responsible to hood or intake elbow damage do to properly aligned intake tube. This system is very large and it clears but it is VERY close.

24: Start engine, let engine run for 30 seconds then turn off engine

21: Resart engine and enjoy!